## Slide 1: Preliminary Results from TPC/Cherenkov Prototype Beam Test at FTBF: B.Azmoun, T.Hemmick, A.Zhang, C.Woody, and SBU Undergrad. Crew

## Slide 2: Detector configuration
Developed CsI coated top GEM at SBU
Shipped detector to FTBF
Si Telescope
TPCC
BEAM
TPC: 10cm drift + 10cmx10cm 4GEM
Cherenkov: 3.3x3.3cm2 pad array +
10cmx10cm 4GEM
Common Gas: CF4
(drift vel = 7.5cm/us & large N0)

## Slide 3: Goals of Beam Test
Overall objective was to demonstrate proof of principle behind the
concept of eID and tracking within a common detector volume
TPC: quantify some performance specs like position and angular resolution
for ~horizontal tracks
Cherenkov: Light yield and eID performance
Look for hit correlations between Cherenkov and TPC detectors

## Slide 4: TPC portion of prototype

## Slide 5
EVENT DISPLAY

## Slide 6
Use Fermi function to determine charge arrival time (Tom convinced me )
EVENT DISPLAY

## Slide 7
EVENT DISPLAY
Often suffer from single pad event cluster in 1 given y-column need good charge sharing for each y-col.

## Slide 8
EVENT DISPLAY
Single pad cluster in first and last y-column
Define vector in 3D using projection on X-Y and Z-Y planes
Use middle of Y column as y-coord.
Define clusters as those pads hit in each y-column
(10 of them in all), then calculate the centroid to give x-coord.
Use middle of Y column as y-coord.
Take a weighted average of charge arrival times in each
y-column cluster to determine z-coord.

## Slide 9
ALL EVENTS
Vector extrapolated to X-Z reference located at Y=pad 10 (ie y=+50cm)
Beating is due to
poor charge sharing
along x-coord.
(removed single pad hits)

## Slide 10
Si and TPC events are not fully sync’d:
N_Ev(TPC)=35798
N_Ev(Si)=20305
No alignment yet done for TPC and Si
Measured angle
=3.3deg.
Data3.1deg.
Cutoff:
see next slide
ALL EVENTS
Vector extrapolated to X-Z reference located at Y=pad 10 (ie y=+50cm)

## Slide 11: Cutoff in beam Z-profile
Y-Z beam profile
Data capture window: ~700ns
 ~50mm
Also, timing resolution from Fermi fit of PA pulse rising edge limits the track reco.
Will consider new track reco. algo.
Used heavy cuts to isolate tracks that were not affected by the cutoff

## Slide 12: Resolutions
Background:
Unsync’d events
The remarkable angular
resolution is artificial

## Slide 13: Cherenkov portion of prototype

## Slide 14: Parameter Scans (initial studies)
Find optimum drift field by maximizing light signal and suppressing signal from ionization
Find light yield by measuring gain curve in both forward bias (to collect charge from ionization) and reverse bias, which collects light signal only. Get FB absolute gain curve by assuming dE/dx = 7keV/cm in CF4.
Npe ~ 10, in line with expectations

## Slide 15: eID performance Vs GEM gain
GEM dV=475V
GEM dV=465V
GEM dV=455V
Used FTBF Cherenkov counters to create trigger for particles above and below Cherenkov threshold
Red curve: TPCC signal from particles below Cherenkov threshold
Blue curve: TPCC signal from particles above Cherenkov threshold

## Slide 16: Hit correlations (Event displays)
TPC hit pixels ~ track
Cherenkov hit pads

## Slide 17: Outlook
Need better Si TPCC event synchronization
Alignment of Si and TPCC reference planes
New TPC track algo.
Cherenkov llight yield Vs radiator length

## Slide 18
Dead channel

## Slide 19
Charge cross sections
EVENT DISPLAY

## Slide 20
Dropped single pad hits

## Slide 22
ALL EVENTS
These results are still very preliminary; need additional fine tuning like setting the data point errors for the fits correctly
Errors on data points are not quite there yet